## Slide 1: Dragon Board™
410c
- Presented by,
Narendran & Pooja Pawade

## Slide 2: Introduction
The Dragon-Board 410c, a product of Arrow Electronics based upon 96-Boards, is the development board based on the mid-tier Qualcomm® APQ8016E processor.
96Boards is a 32-bit and 64-bit ARM® Open Platform hosted by Linaro™ with the intension to serve the software/ maker and embedded OEM communities
Dragon-Board 410c is designed to support rapid software development, education and prototyping

## Slide 3: FRont view

## Slide 4: Back view

## Slide 5: SPECIFICAION Features
OS Support:
      Android 5.1 (Lollipop) on Linux Kernel 3.10
      Linux based on Debian 8.0
      Open Embedded
      Ubuntu Core
      Windows 10 IoT Core
CPU:
      Quad-core ARM® Cortex® A53 at up to 1.2 GHz per core with both 32-bit and 64-bit support.
      Qualcomm Adreno 306 400MHz GPU for PC-class graphics with support for advanced APIs, including OpenGL ES.
Memory/storages:
1GB LPDDR3 533MHz / 8GB eMMC 4.5 / SD 3.0 (UHS-I)

## Slide 6: Continue..
Graphics:
Qualcomm Adreno 306 GPU with support for advanced APIs, including OpenGL ES 3.0, OpenCL, DirectX, and content security.
Video:
1080p@30fps HD video playback and capture with H.264 (AVC), and 720p playback with H.265 (HEVC)
Camera Support:
Integrated ISP with support for image sensors up to 13MP
Audio:
PCM/AAC+/MP3/WMA, ECNS, Audio+ post-processing (optional)

## Slide 7: CONTINUE..
Connectivity:
      WLAN 802.11 b/g/n 2.4GHz
      Bluetooth 4.1
      GPS
      On-board GPS antenna
      On-Board Bt and WLAN antenna
User Interface:
      Power/Reset
      Volume Up/Down
      6 LED Indicators:
        4 user controllable
        2 for radios (BT and WLAN activity)

## Slide 8: Continue..
I/O Interface:
One USB 2.0 micro B (device mode only)
Two USB 2.0 (host mode only)
One 40-pin Low Speed (LS) expansion connector UART, SPI, I2S, I2C x2, GPIO x12, DC power
One 60-pin High Speed (HS) expansion connector 4L-MIPI DSI, USB, I2C x2, 2L+4LMIPI CSI
Footprint for one optional 16-pin analog expansion connector for stereo headset/ line-out, speaker and analog line-in
The board can be made compatible with Arduino using an add-on mezzanine board

## Slide 9: Continue..
Power, Mechanical and Environment:
  Power: +6.5V to +18V
  Dimensions: 54mm by 85mm meeting 96Boards™ Consumer Edition standard dimensions specifications
  Operating Temp: 0°C to +70°C
  RoHS and Reach compliant
External Storage:
  Micro SD card slot

## Slide 10: ApplicaTions
Robotics
Cameras
Medical Devices
Vending machine
Smart Building
Digital Signage
Casino Gaming console

## Slide 11: Conclusion
Processor, WLAN, Bluetooth, and GPS all packed into a board the size of a credit card.
All this makes it ideal for enabling embedded computing and Internet of Things (IoT) products
It is designed to support feature-rich functionality, including multimedia, Game development etc.,

## Slide 12: Thank you...!